## Slide 1
Geomorphological Hazards of Slopes
Introduction: Hazard, Risk and Classification
Day 1 | Session 1 | Geomorphological Hazards of Slopes | Uni. Silesia, Katowice | Ola Fredin (NTNU)

## Slide 2
Course overview
16 hours over 3 days: Day 1 — fundamentals; Day 2 — stability & triggers; Day 3 — runout & mapping
8 Jupyter Notebooks run in parallel with the lectures — theory on the slides, computation in the notebooks
Regional focus: Carpathians, Tatras, Sudetes, Norwegian fjord slopes and global hotspots
Assessment: notebook portfolio submitted after the course (2 ECTS)
Software: Python 3.11+, QGIS 3.34 LTR

## Slide 3
§1
What is a geohazard?

## Slide 4
Hazard, vulnerability, exposure, risk
Geohazard: a natural process capable of causing harm to people, property or the environment
Varnes (1984) / UN-DHA decomposition: R = H × V × E
H (Hazard) — probability of a damaging event of given magnitude at a given location and time
V (Vulnerability) — fraction of value lost when the event occurs [0, 1]
E (Exposure) — value of people and assets in the hazard zone
R (Risk) — expected loss per unit time (currency per year, or lives per year)
The three terms come from three different communities: geologists estimate H, engineers V, planners E

## Slide 5
The risk equation
Varnes (1984) / UN International Strategy for Disaster Reduction:
R = H × V × E
H — hazard probability (what the next 7 notebooks quantify)
V — vulnerability fraction (engineering and social science)
E — exposure value (spatial planning and census data)
Practical consequence:
Reducing R requires reducing at least one of H, V or E. Risk can be managed even when H is fixed.
Reference: Varnes (1984); UN-DHA (1992) RADIUS framework

## Slide 6
§2
Magnitude–frequency relationships

## Slide 7
Landslide magnitude–frequency: a power law
Chart: Landslide area (m², log scale)
| 0.1 | 0.4 | 1.6 | 6.3 | 25 | 100 | 400 | 1600 | 6300 | 25000 | 100000
Cumulative N(>A) | 100000 | 25000 | 6300 | 1600 | 400 | 100 | 25 | 6.3 | 1.6 | 0.4 | 0.1
Schematic power law N ∝ A^(−1.2) after Malamud et al. (2004) — Italian, US and Guatemalan inventories

## Slide 8
Why the power law matters
Above ~100–1000 m² area: cumulative event count scales as N(>A) ∝ A^(−b), b ≈ 1.0–1.5
Small events are the most frequent, but large events dominate cumulative sediment flux
Rollover at small sizes: physical suppression by cohesion + root strength, and under-mapping
Design return periods (10, 100, 500 yr) must account for this frequency distribution
Malamud et al. (2004): same exponent across Italy, the US and Guatemala → universal process

## Slide 9
§3
Landslide classification

## Slide 10
Why classify? The Varnes–Hungr framework
A classification is a shared language: geologists, engineers and planners communicate unambiguously
Varnes (1978): movement-type × material grid — still the international standard
Hungr, Leroueil & Picarelli (2014) updated it to 32 named types; eliminates ambiguous hybrids
Each type carries characteristic velocity, runout ratio H/L, water content, and failure mechanism
Course notebooks address 5 types: rock fall, debris fall, translational slide, debris flow, earth flow

## Slide 11
Movement types (Hungr et al. 2014)
Movement type
Fall: detachment from steep face; free fall and bouncing
Topple: rotation about a pivot at the block base
Slide (rotational): curved slip surface — spoon-shaped scar
Slide (translational): planar slip surface parallel to slope
Spread: lateral extension, generally in sensitive clays
Flow: plastic deformation — debris flow, earth flow
Material and properties
Material: rock, debris (mixed coarse + fine), earth (fine-grained)
Velocity classes (WP/WLI): extremely slow (<16 mm/yr) to extremely rapid (>5 m/s)
Runout ratio H/L: rock falls ~0.6, rock avalanches <0.3, debris flows 0.2–0.5
Notebook 01 exercise: locate each type on the classification matrix

## Slide 12
Regional context: Central Europe
Carpathians: flysch sequences (sandstone–shale alternations) predisposed to translational sliding; ~5000 mapped slides in Poland alone (CGS inventory)
Tatras: steep glacially-carved valley walls; abundant rock fall and debris flows on talus cones
Sudetes: crystalline basement with deep weathering; slow earth flows in loess cover
Trigger regime: frontal rainfall systems + orographic enhancement — daily rainfall records frequently exceeded
Carpathian villages built on fan deposits: the deposit is evidence of past runout

## Slide 13
Regional context: Norwegian fjord slopes
Fjord walls reach 1000–1400 m above sea level with slope angles 35–55°
Rock avalanches: Åknes (8 Mm³ actively deforming), Mannen — national early-warning systems
Quick-clay slides: Rissa 1978, Gjerdrum 2020 (10 fatalities)
Debris flows: steep gullied hillslopes after short high-intensity summer storms
Infrastructure challenge: roads and railways hug the fjord shore — directly in runout paths

## Slide 14
Jupyter Notebook 01
Geohazards: Hazard, Risk and Classification
Interactive R = H × V × E calculator — vary each component and watch R respond
Magnitude–frequency plot: fit a power law to a synthetic inventory
Classification matrix: place the 8 main process types in the Hungr et al. (2014) grid
Case study: 2010 Bieszczady (Carpathians) slides — assign type, estimate H and E
Output figures: risk_decomposition.svg, magnitude_frequency.svg, classification_matrix.svg

## Slide 15
Key Points & References
R = H × V × E decomposes risk into estimable components from three communities
Landslide populations obey a power-law magnitude–frequency distribution (b ≈ 1.2)
Hungr et al. (2014) gives 32 named process types — use the movement × material grid
Carpathians: translational failures in flysch dominate
Norwegian fjord slopes: rock avalanches and quick-clay as additional major hazard types
The rest of the course quantifies H — notebooks 02–08
Selected references
Varnes DJ (1984) USGS Open-File Rep. 84-760
Hungr O, Leroueil S, Picarelli L (2014) Landslides 11: 167-194
Malamud BD et al. (2004) Geophys. Res. Lett. 31: L15501
Wieczorek GF & Glade T (2005) in: Debris-Flow Hazards
Furseth A (2006) Skredulykker i Norge. Tun Forlag