## Slide 1
LiDAR, Hillshade and Susceptibility Mapping
Seeing through the forest: from point cloud to hazard map
Day 3 | Session 3 | Geomorphological Hazards of Slopes | Uni. Silesia, Katowice | Ola Fredin (NTNU)

## Slide 2
Why LiDAR changed geomorphological mapping
Before LiDAR: photogrammetric DEMs at 5–20 m resolution, obscured by forest canopy
Airborne LiDAR: 1–10 pulses/m²; multi-return separates ground from vegetation; bare-earth DTM at 1–2 m
At 1 m resolution: scarps, crowns, headscarps, terraces, lobes, pressure ridges — all visible through forest
Poland ISOK: national 0.6 pts/m² coverage (2013–2014), freely available at geoportal.gov.pl
Norway hoydedata.no: 2 pts/m² national coverage, updated regionally to 5–10 pts/m²
Revolution: national-scale landslide inventory mapping now feasible from a desktop GIS

## Slide 3
§1
From raw LiDAR to bare-earth DTM

## Slide 4
The LiDAR processing chain
Raw data: point cloud (LAS/LAZ format); each point has X, Y, Z, intensity, return number
Classification: first-return = top of canopy; last-return ≈ ground; ASPRS ground class
Bare-earth DTM: interpolate ground-classified points → raster at 0.5–2 m (TIN or IDW)
Products: DTM (ground only), DSM (surface), CHM = DSM − DTM
QGIS tools: LAStools plugin, PDAL pipeline, or WhiteboxTools
Quality check: compare to surveyed ground control points; RMSE < 15 cm for ISOK data

## Slide 5
Hillshade and multi-azimuth illumination
Standard hillshade: single sun azimuth 315°, altitude 45° — fast but directional shadows hide features
Multi-azimuth hillshade: average of hillshades from 8 azimuths (0°, 45°, …, 315°) at 45° altitude
Sky-view factor (SVF): fraction of visible sky dome at each point (Kokalj et al. 2011) — best for subtle morphology
Local Relief Model (LRM): DTM minus a smoothed trend — highlights small-scale features
Best practice: SVF or LRM + hillshade as overlay → identify scarps, toe bulges, back-tilted blocks
QGIS: Raster → Terrain Analysis → Hillshade; or Relief Visualisation Toolbox (RVT) plugin

## Slide 6
§2
Landslide inventory mapping

## Slide 7
Building a landslide inventory from LiDAR
Mapping units: point (centroid), polygon (outline), source + transport + deposit (three shapefiles)
Attribute schema (minimum): landslide ID, type (Hungr 2014), date/period, area, volume, data source
Mapping cues in LiDAR hillshade: arcuate or linear scarp, hummocky deposit, elongated lobe, back-tilted trees
Multi-temporal: overlay two LiDAR epochs to detect reactivation and new events (change detection)
Validation: field check a stratified random sample (10–20% of inventory) for type confirmation
QGIS lab (Notebook 08): digitise sources, tracks, deposits on a 1 m Tatra DTM

## Slide 8
Susceptibility mapping approaches
Heuristic / geomorphological: overlay slope angle, lithology, land cover, LiDAR-mapped scarps — expert scoring
Statistical: logistic regression, weight-of-evidence, random forest — train on inventory, predict spatially
Physics-based: infinite-slope FS mapped across DEM with spatially variable soil parameters (SHALSTAB, TRIGRS)
Hybrid: physics-based FS as predictor variable in a statistical model
Performance: ROC/AUC; spatial cross-validation essential (data are spatially autocorrelated)
Output: susceptibility index map classified as low / medium / high / very high

## Slide 9
α–β on a DEM profile: Notebooks 07 → 08
DEM workflow
QGIS Profile Tool: extract elevation along a digitised centreline
Identify fan apex (slope < 15°) → measure β from the DTM profile
Compute: tanα = a tanβ + b (Nora Andreassen NTNU 2026 coefficients)
Project the α line from source → predicted stopping distance
Compare to mapped deposit extent → validate α–β for this site
Lab deliverables (Notebook 08)
Notebook 08 deliverables:
Hillshade map with digitised sources, tracks, deposits overlaid
Three shapefiles with consistent attribute schema
β measurements and predicted α runout distances (Python cell)
One-paragraph interpretation: how well does α–β predict observed runout?
Submit as zip (shapefiles + screenshot + notebook)

## Slide 10
Course synthesis: from Terzaghi to the hazard map
Lecture 1: R = H × V × E — what we are trying to estimate
Lectures 2–3: σ′ = σ − u and τ_f = c′ + σ′ tanφ′ — the physics of failure
Lecture 4: FS equation — translating stress state into a scalar stability index
Lecture 5: FS(t) — rainfall drives pore pressure; ID thresholds capture it empirically
Lectures 6–7: once failure occurs → trajectory, runout, hazard zone
Lecture 8: LiDAR reveals evidence of past events; GIS maps future hazard
The DEM contains everything: slope angle, curvature, flow direction, contributing area

## Slide 11
Key Points & References
LiDAR bare-earth DTMs at 1–2 m reveal landslide morphology through forest
Multi-azimuth hillshade / SVF / LRM: best for scarp and lobe identification
Inventory: three-layer shapefile (source / track / deposit) + attribute schema
Susceptibility: heuristic → statistical → physics-based; validate with ROC/AUC
α–β on DEM profile: connects debris-flow runout theory (NB 07) to field data (NB 08)
Full chain: Terzaghi → FS → rainfall trigger → runout → LiDAR map → hazard zone
Selected references
Jaboyedoff M et al. (2012) Nat. Hazards 61: 5-28
Kokalj Ž et al. (2011) Remote Sens. 3: 398-415
Guzzetti F et al. (2012) Earth-Sci. Rev. 112: 42-66
Van Westen CJ (2013) Treatise on Geomorphology vol. 3
Andreassen N (NTNU, 2026) MSc thesis — α–β coefficients for Norwegian debris flows (unpubl.)